Registers are prefixed with an R to make the code more human-readable.

The mnemonics and opcodes in order:

ADD	0x0
ADC	0x1
SUB	0x2
SBC	0x3
LSH	0x4
LSC	0x5
RSH	0x6
RSC	0x7
XOR	0x8
NAND	0x9
LI	0xA
MOV	0xB
JALR	0xC
BEQ	0xD
INT	0xE
RINT	0xF

The register layout is as follows:

32-bit Reg Address	8-bit Reg Addresses
0x0	0x0	0x1	0x2	0x3
0x1	0x4	0x5	0x6	0x7
0x2	0x8	0x9	0xA	0xB
0x3	0xC	0xD	0xE	0xF

ADD <Reg B>, <Reg C>, <Reg A>

Example:
ADD R3, R6, R4

This adds R6 to R3 then stores the result in R4. If the result is larger than 255, the carry flag is set.

ADC <Reg B>, <Reg C>, <Reg A>

Example:
 ADC RA, RB, R3

This adds RB and the carry flag to RA then stores the result in R3. If the result is larger than 255, the carry flag is set.
SUB <Reg B>, <Reg C>, <Reg A>

Example: SUB RF, R2, R1

This subtracts R2 from RF and stores the result in R1. If the result is less than 0, the carry flag is set.

SBC <Reg B>, <Reg C>, <Reg A>

Example:
SBC RF, R2, R1

This subtracts R2 and the carry flag from RF then stores the result in R1. If the result is less than 0, the carry flag is set.

LSH <Reg A>

Example:
LSH RA

This shifts RA left by one bit then stores the result back in RA. If the MSB is 1, the carry flag is set.

LSC <Reg A>

Example:
LSC R3

This shifts R3 left by one bit and ORs the LSB with the carry flag then stores the result back in R3. If the MSB is 1, the carry flag is set.

RSH <Reg A>

Example:
RSH R7

This shifts R7 right by one bit then stores the result in R7. If the LSB is 1, the carry flag is set.

RSC <Reg A>

Example:
RSC R0

This shifts R0 right by one bit and ORs the MSB with the carry flag then stores the result back in R3. If the LSB is 1, the carry flag is set.

XOR <Reg B>, <Reg C>, <Reg A>

Example:
XOR RD, R1, R3

This XORs RD with R1 and stores the result in R3.

NAND <Reg A>, <Reg C>, <Reg A>

Example:
NAND R2, R9, RD

This NANDs R2 with R9 and stores the result in RD.

LI <IMM>, <Reg A>

Example:
LI 0xF7, R5

This loads 0xF7 into R5.

NOTE: In all MOV operations, Reg A is a 2-bit register address.

MOVS <Reg C>, <Reg A>, [T|F]

Example:
MOVS R8, R0, F

This moves the value in R8 to the memory location at the address in 32-bit register R0 and does not increment the value in R0.

MOVL <Reg C>, <Reg A>, [T|F]

Example:
MOVL RA, R3, T

This moves the value in RA to the memory location at the address in 32-bit register R0 and increments the value in R0.

MOVR <Reg B>, <Reg C>

Example:
MOVR R5, R9

This moves the value in R5 to R9.

MOVI <IMM>, <Reg A>

Example:
MOVI 0x17, R2

This moves the literal 0x17 into the memory location at the address in 32-bit register R2.

JALR <Reg D>, <Reg A>

Example:
JALR R0, R2

This loads the PC into R0 then stores the value in R2 to the PC.

BEQ <Reg B>, <Reg C>, <Reg D>, <Reg A>

Example:
BEQ R7, RF, R0, R1

This XORs R7 with RF. If the result is 0, the PC is loaded into 32-bit register R1 and the value in the 32-bit register R0 is loaded into the PC. If, however, both registers were R0 then the PC would not be loaded into any register.

INT <Reg A>

Example:
INT 0x05

This pushes the PC onto the interrupt stack and shifts 0x05 left 8 bits, then ORs it with 0xFFFF0000, and stores the resulting value in the PC. The interrupt depth counter is then incremented.

RINT

Example:
RINT

This pops the top value from the interrupt stack into the PC and decrements the interrupt depth counter.

The following are not instructions but are assembler directives:

.imm <label>, <IMM>

This tells the assembler to replace all instances of <label> with <IMM> (label being a string of text, IMM being an 8 or 32-bit immediate [also known as “literal”] value).

.variable <name>, <address>

This tells the assembler to replace all instances of variable <name> with the address <address> (name being the variable name, address being a 32-bit literal or a label).

<label>:

This tells the assembler to replace all instances of <label> with the address that the label is located at in code.