SIMP-8
Simple Integrated Machine for Processing, 8-bit
ISA Revision 0

The SIMP-8 architecture has been designed with simplistic versatility in mind. It features a 16 opcode instruction set with facilities in place to support large number calculations. The instructions are variable width (7 one-byte, 9 two-byte). The address bus is 32 bits wide to allow for a 4G address space, bringing it to relatively modern standards in terms of the amount of memory addressable. The data bus is 8 bits wide, doubling as an interrupt vector input for hardware interrupts (which are triggered by a single pin input).

There are 16 8-bit general purpose registers which can either be addressed individually or as one of 4 32-bit registers (for addressing). The register setup is as follows:

32-bit Reg Address	8-bit Reg Addresses
0x0	0x0	0x1	0x2	0x3
0x1	0x4	0x5	0x6	0x7
0x2	0x8	0x9	0xA	0xB
0x3	0xC	0xD	0xE	0xF

The data organization for each instruction and a description of their functionality is as follows. Each block represents 4 bits (excluding mnemonic, which is merely an identifier):

MNEMONIC	OPCODE	BLOCK A		BLOCK B	BLOCK C
ADD	0x0	Reg A		Reg B	Reg C
ADC	0x1	Reg A		Reg B	Reg C
SUB	0x2	Reg A		Reg B	Reg C
SBC	0x3	Reg A		Reg B	Reg C
LSH	0x4	Reg A		N/A
LSC	0x5	Reg A		N/A
RSH	0x6	Reg A		N/A
RSC	0x7	Reg A		N/A
XOR	0x8	Reg A		Reg B	Reg C
NAND	0x9	Reg A		Reg B	Reg C
LI	0xA	Reg A		IMMEDIATE
MOV	0xB	OPCODE PT. 2*		*	*
JALR	0xC	Reg A	Reg D	N/A
BEQ	0xD	Reg A	Reg D	Reg B	Reg C
INT	0xE	Reg A		N/A
RINT	0xF	Don't care, but convention is 0 to prevent future incompatibility		N/A

ADD: Add Reg C to Reg B and store result in Reg A
ADC: Add Reg C and carry bit to Reg B and store result in Reg A

SUB: Subtract Reg C from Reg B and store result in Reg A
SBC: Subtract Reg C and carry bit from Reg B and store result in Reg A

LSH: Shift bits in Reg A by one position to the left and store result in Reg A
LSC: Shift bits in Reg A by one position to the left, placing the carry bit into the LSB position and store result in Reg A

RSH: Shift bits in Reg A by one position to the right and store result in Reg A
RSH: Shift bits in Reg A by one position to the right, placing the carry bit into the MSB position and store result in Reg A

XOR: Bitwise XOR Reg C with Reg B and store result in Reg A
NAND: Bitwise NAND Reg C with Reg B and store result in Reg A

LI: Load 8-bit immediate into Reg A

MOV: The MOV instruction has a secondary opcode component to allow for more operations involving data transfer. The codes are as follows:

0xB	0	Reg A	Inc	RESERVED	Reg C
0xB	1	Reg A	Inc	RESERVED	Reg C
0xB	2	RESERVED	Reg B		Reg C
0xB	3	Reg A	IMMEDIATE

MOV 0: Move data in Reg C to address in Reg A, if Inc bit set then increment Reg A
MOV 1: Move data at address in Reg A to Reg C, if Inc bit set then increment Reg A
MOV 2: Move data in Reg C to Reg A
MOV 3: Move 8-bit immediate to address in Reg A

JALR: Store PC in Reg A and load Reg D into PC
BEQ: If Reg C is equal to Reg B then load PC into Reg A and load Reg D into PC. If Reg A and Reg D are the same, skip storing initial PC

INT: Jump to interrupt vector held in Reg A, load PC into interrupt stack, and incrementing interrupt depth counter.
RINT: Pop top value from interrupt stack into PC and decrement interrupt depth counter

As you may have guessed, the “reserved” bits are currently a “don't care”, however they may be used later for something so standard convention is to simply fill them with 0's to avoid future compatibility issues.
Interrupts are addressed with an 8-bit interrupt vector, either grabbed from the data bus (in the case of a hardware interrupt) or from a register (as with software interrupts) and used as the second least significant byte of the actual address to be loaded into the program counter. The high two bytes of the interrupt address are 0xFFFF, thus putting the interrupt code somewhere that will likely not be used or executed to under normal operating conditions. An interrupt may be as long as it needs to be (until you run out of interrupt code space [64KB {split into 256 256B chunks}]) and may run into the next interrupt vector's code space. If the PC hits the end without a RINT instruction, however, it will roll over to 0x00000000 and restart the system. Depending on how your code is set up, memory stored in RAM already may cause erratic, undefined behavior.

# NOTE: THIS DOCUMENT IS A WORK IN PROGRESS